## Slide 1
Reservoir-Volume Characterization
Method, findings, and a defensible field strategy across 7 wells
Kamil Muradli · eiGroup Associate Data Scientist assessment · May 2026

## Slide 2
Three QC findings that shape every downstream decision
Caught at load-time, surfaced in every metric
• well_3: 78 NaN porosity samples (4%) → excluded from net, counted separately
• well_5: logged at 0.5 m spacing; others at 0.2 m → dz computed per-well
• ALL 7 wells: 15-30% of samples at the 15,000 mD permeability cap
•
• Saturation matters most: it makes kh estimates a LOWER BOUND, not a best estimate
• Each finding surfaces as a counter column in every downstream metric
• QC is not paperwork — it drives the credibility of every number that follows
→ The QC step is the source of every caveat in this analysis.
2 / 19

## Slide 3
Net-to-Gross by zone tells the geological story
• Zone B dominates: 93% NTG, 10× the kh of any other zone
• Zone D: 10% NTG everywhere — tight rock, not reservoir
• Zone C: silent second story (84% NTG, 680K mD·m)
• Same pattern in all 7 wells — geology is reproducible
•
• Field volume = sum of (zone × well) kh contributions
• Operational ranking: B → C → E → A → D
→ NTG is more diagnostic than any single permeability number.
3 / 19

## Slide 4
Cutoff sensitivity tells us which volumes are brittle
• Zone B NTG: stable across the full sweep (range only 0.11)
• Zone A NTG: highly sensitive (0.15 → 0.95 across 0.30-0.70 cutoffs)
• Knee for all zones at vsh ≈ 0.35 (same in all 7 wells)
• Default cutoff (0.5) sits on the flat part of each curve
•
• Zone B is the MOST defensible volume estimate in the field
→ Zone B's volume estimate doesn't depend on cutoff choice — that's robustness.
4 / 19

## Slide 5
When 'homogeneous' is an instrument artefact
Lorenz curves expose tool censoring
• Zone C: L = 0.65 — genuinely heterogeneous, top 30% delivers 80% of kh
• Zone E: L = 0.52, Zone A: L = 0.46 — moderate heterogeneity
• Zone B: L = 0.00 — but this is a TOOL ARTEFACT, not homogeneity
•
• 88% of Zone B samples are at the 15,000 mD cap
• The Lorenz curve flattens into the 45° diagonal mechanically
• Lesson: don't interpret Lorenz on censored data
→ The strongest signal of saturation isn't a number — it's a flat Lorenz curve.
5 / 19

## Slide 6
Saturation pollutes well rankings
• well_7 ranks #1 by kh (2.59 M) — but 30% tool-capped
• well_1 ranks #2 (2.27 M) — 25% tool-capped
• wells 2/4/5/6 at 14-15% saturation — more defensible 'best wells'
•
• ⚠ marker in heatmap = saturation count per (well, zone)
•
• Production fix: saturation-weighted kh ranking
• Long-term fix: uncensored perm tool + core calibration
→ The highest-kh well may just be the most censored well.
6 / 19

## Slide 7
Zone D should be bypassed
Tight rock, not reservoir — fails on porosity, not shale
• Zone D NTG never exceeds 32% — even at the loosest cutoff (vsh ≤ 0.7)
• avg phit in Zone D = 0.092 — right at the phit cutoff (0.08)
• Samples fail the POROSITY test, not the shale test
• No matter how generous the shale tolerance, Zone D is not reservoir
•
• All 7 wells: same finding
• Operational implication: skip Zone D in volume calculations
• Don't drill into it; don't model it; document the bypass decision
→ Bypassing Zone D is unambiguous. The geology says so.
7 / 19

## Slide 8
Where our kh estimates are most uncertain
Bootstrap confidence intervals: precision vs accuracy
• Method: 200 resamples per (well, zone) group, 90% percentile CI
• Most groups: tight CIs (high sample counts, low variance)
• Zone D: wide CI relative to point estimate — but magnitudes are tiny
• Zone B: tight CI — but high SAMPLING precision doesn't fix saturation BIAS
•
• Bootstrap measures sampling uncertainty, not measurement bias
• A censored tool is a measurement bias the bootstrap can't see
• Saturation remains the dominant uncertainty in Zone B kh
→ Our numbers are PRECISE. Whether they're ACCURATE depends on the tool — different problem.
8 / 19

## Slide 9
Two clustering attempts: Zone B failed (instructive), Zone C worked
Method awareness: knowing when not to trust your own model
Zone B (initial target)
• Highest kh, highest NTG — obvious first choice
• Silhouette peaks at k=2 (0.65), drops at k=3
• But: two clusters have IDENTICAL centroids
• – vsh 0.243 vs 0.233 (Δ = 0.01)
• – log_perm 4.17 vs 4.16
• – 96% saturated in EVERY sub-zone
• LOWO ARI = 0.97 — reproducibly meaningless
Zone C (re-targeted)
• <1% saturation — clean signal
• Real Lorenz = 0.65 (Slide 5)
• NTG 84%, kh 680K, all 7 wells
• 3 sub-zones with 5× perm separation
• Same vertical stack in every well
• LOWO ARI = 0.97 — meaningfully reproducible
→ Clustering can only see what the tool measures. When tools are censored, clusters reproduce the censoring.
9 / 19

## Slide 10
Zone C splits into 3 reproducible sub-zones
Three rock types, one geological column, 7 wells
• Sub-zone 0: tight (~200 mD, phit 0.14, vsh 0.45)
• Sub-zone 1: mid (~700 mD, phit 0.21, vsh 0.34)
• Sub-zone 2: best (~1,100 mD, phit 0.23, vsh 0.29)
•
• Vertical stack consistent across all 7 wells:
• – Best on top · tight in middle · mid at base
• LOWO Adjusted Rand Index = 0.95–0.99
→ Three orders of magnitude separation. Same stack in every well. Real geology.
10 / 19

## Slide 11
Sub-zone 2 is the drilling target
29% of Zone C thickness — 48% of Zone C flow capacity
• Sub-zone 2 thickness: 315.6 m total across 7 wells (29% of Zone C)
• Sub-zone 2 kh: 350 K mD·m (48% of Zone C)
• Geological location: TOP of Zone C in every well
• Saturation: <1% — the 1,100 mD estimate is defensible
•
• Completion implication: place perforations in the top third of Zone C
•
• Drilling implication: vertical wells targeting Zone C should land at sub-zone 2 depth
• Risk: minimal — geology reproduces across all 7 wells
→ The clearest operational recommendation in this whole analysis.
11 / 19

## Slide 12
k=3 by geological intuition, not by silhouette pick
Choosing the number of clusters — defensibly
• Silhouette ranks k=2 highest in both zones (0.65 / 0.39)
• BIC monotonically prefers higher k (GMM overfits noise)
•
• We chose k=3 for geological reasons:
• – Three lithology classes standard in clastics
• – At k=3 Zone C centroids separate 5× in perm
• – At k=2 two real lithologies collapse together
• – At k=4 we'd be splitting noise
•
• Post-hoc validation: log_perm centroids 1.92, 2.44, 2.65
→ Don't outsource the lithology count to a silhouette score.
12 / 19

## Slide 13
Production-ready engineering
Single-command reproducible pipeline, fully tested
• 105 pytest tests across 6 modules
• 96-100% coverage on hot paths
• – metrics: 99%, sensitivity: 96%
• – clustering: 97%, viz: 100%
•
• Single-command CLI:
• quality → metrics → sweep → field → subzones
•
• Every chart: matplotlib PNG + Plotly HTML
• Reproducible from raw CSVs in 5 commands
→ This is a pipeline, not a notebook — re-runnable when new wells arrive.
13 / 19

## Slide 14
Five decisions this analysis supports
• Treat Zone B kh as a CONSERVATIVE LOWER BOUND — not a best estimate
•
• BYPASS Zone D — it's tight rock, not reservoir
•
• TARGET sub-zone 2 (top of Zone C) for drilling and completion
•
• RE-RANK wells using saturation-weighted kh, not raw kh
•
• CALIBRATE Zone A and Zone C cutoffs to core data before publishing volumes
→ Happy to go deep on any of these — and to discuss what I'd do differently with more data.
14 / 19

## Slide 15
Backup: bootstrap method details
• Per (well, zone) group, 200 resamples with replacement
• Within each resample: apply same net cutoffs (vsh ≤ 0.5, phit ≥ 0.08)
• kh = Σ(perm × dz) on the resampled net interval
• Report kh mean + 5th/95th percentiles = 90% CI
• Seed = 42 for reproducibility
•
• Cost: 35 groups × 200 resamples × 3 cutoffs ≈ 21,000 kh calculations (~10s)
• Optional via CLI: python -m src.cli sweep --bootstrap
15 / 19

## Slide 16
Backup: clustering smoothing rationale
• Problem: sample-level clustering produces 1-sample label flips
• Real geological units are continuous, metres-thick
•
• Step 1 — rolling mode (window=11, ~2.2 m at 0.2 m sampling):
• Each sample's label is the mode of itself and ±5 neighbours
•
• Step 2 — absorb short runs (min_run_length=5):
• Any uninterrupted run shorter than 5 samples (1 m)
• is merged into the longer neighbouring run
•
• Per-well processing — depth ordering doesn't cross well boundaries
16 / 19

## Slide 17
Backup: why pooled clustering, not per-well
• Alternative: cluster each well independently, then 'match' labels
• Problem: KMeans 'cluster 0' in well 1 is unrelated to 'cluster 0' in well 2
• Matching requires Hungarian algorithm or similar — complex, brittle
•
• Pooled approach: fit ONE model on all wells' Zone C samples
• Every sample gets a label in the same space
• Cluster ID = rock type, globally
•
• Cross-well consistency tested via leave-one-well-out (ARI)
• Trade-off: assumes the same rock types exist in every well
• – validated by the 0.97 LOWO ARI
17 / 19

## Slide 18
Backup: stable label ordering via log_perm
• KMeans labels are arbitrary — re-running may swap labels
• Without reordering: 'sub-zone 2' could be tight in one run, best in next
•
• Solution: after fitting, compute mean log_perm per cluster
• Relabel so cluster 0 = lowest mean log_perm, k-1 = highest
•
• Guarantees: across runs, across LOWO folds, the same
• cluster ID corresponds to the same rock type
•
• Simpler than Hungarian-assignment matching
• Stable when features include log_perm (which they do)
18 / 19

## Slide 19
Backup: what I'd add with more data
• Core measurements at saturated depths:
• – Calibrate the 15,000 mD cap → uncensored perm distribution
• – Lab phit / vsh check → calibrate net cutoffs
•
• Production data:
• – Correlate kh estimates with measured production rates
• – Validate sub-zone 2 as drilling target empirically
•
• Seismic horizons:
• – Geological correlation across wells
• – Confirm sub-zone vertical stacking is geological, not statistical
•
• Censored regression to recover real perm from (phit, vsh) in saturated samples
19 / 19